## Slide 1: TCP/IP

## Slide 2: TCP/IP Protocol Suite
TCP/IP stands for Transmission Control Protocol/Internet Protocol and is a suite of communication protocols used to interconnect network devices on the internet. TCP/IP is also used as a communications protocol in a private computer network (an intranet or extranet).
The entire IP suite -- a set of rules and procedures -- is commonly referred to as TCP/IP. TCP and IP are the two main protocols, though others are included in the suite. The TCP/IP protocol suite functions as an abstraction layer between internet applications and the routing and switching fabric.

## Slide 3: The 4 layers of the TCP/IP model
The application layer provides applications with standardized data exchange. Its protocols include HTTP, FTP, Post Office Protocol 3, Simple Mail Transfer Protocol and Simple Network Management Protocol. At the application layer, the payload is the actual application data.
The transport layer is responsible for maintaining end-to-end communications across the network. TCP handles communications between hosts and provides flow control, multiplexing and reliability. The transport protocols include TCP and User Datagram Protocol, which is sometimes used instead of TCP for special purposes.

## Slide 4: The 4 layers of the TCP/IP model
The network layer, also called the internet layer, deals with packets and connects independent networks to transport the packets across network boundaries. The network layer protocols are IP and Internet Control Message Protocol, which is used for error reporting.
The physical layer, also known as the network interface layer or data link layer, consists of protocols that operate only on a link -- the network component that interconnects nodes or hosts in the network. The protocols in this lowest layer include Ethernet for local area networks and Address Resolution Protocol.

## Slide 5: TCP/IP Protocols
Application layer - HTTP, FTP, Telnet, SMTP, DNS, etc.
Transport layer - TCP (reliable stream, ports, flow control, congestion control), UDP
Network layer - IP, ICMP, IPv6 (routing)
Data Link layer - PPP, Ethernet, ATM, etc. (channel sharing)

## Slide 6: Packet structure
+------------------+----------------+------------------+---------------+
| Data Link header | Network header | Transport header | Appl. Data... |
+------------------+----------------+------------------+---------------+

## Slide 7: UDP Header
Header (8 bytes)
Source port, 16 bits (0-65535)
Destination port, 16 bits (0-65535)
Length in bytes, 16 bits (0-65535)
Checksum, XOR of header, 16 bits
If the header checksum fails, the packet is discarded. The data is not error checked.

## Slide 8: TCP header
TCP header (20 bytes)
Source port, 16 bits (0-65535)
Destination port, 16 bits (0-65535)
Sequence number, 32 bits, number of bytes sent
Acknowledgment number, 32 bits, number of bytes received
Header length, 8 bits = 40 unless options are used
Unused, 2 bits
URG, 1 bit, unused
ACK, 1 bit, 1 = received sequence through acknowledgment number
PSH, 1 bit, unused
RST, 1 bit
SYN, 1 bit, 1 = opening connection
FIN, 1 bit, 1 = closing connection
Receiver window size, 16 bits (bytes free in buffer, scaled using option in setup)
Checksum, 16 bits (XOR of header only)
Urgent pointer, 16 bits, unused
Options, variable length (usually 0)
Data, variable length (usually 0-1500)
Underlying network layer provides an unreliable packet delivery service. Packets may be lost, duplicated, or delivered out of order.

## Slide 9: 3-way Handshake
Reliable stream
Protocol to ensure that all packets are received, and in the correct order.
Sender sends packet, waits for ACK
Receiver replies with ACK, seq. number
Sender marks data as sent
If checksum fails, packet is discarded
If ACK times out, sender retransmits all unmarked data
If same packet is ACKed 3 times, sender resends next packet (fast resend)
Receiver ACKs all packets, including duplicates

## Slide 10: IP
An IP header is header information at the beginning of an Internet Protocol (IP) packet. An IP packet is the smallest message entity exchanged via the Internet Protocol across an IP network. IP packets consist of a header for addressing and routing, and a payload for user data. The header contains information about IP version, source IP address, destination IP address, time-to-live, etc. The payload of an IP packet is typically a datagram or segment of the higher-level transport layer protocol, but may be data for an internet layer (e.g., ICMP or ICMPv6) or link layer (e.g., OSPF) instead.
Header (20 bytes)
Version, 4 bits, IPv4 = 4
Header length, 4 bits, 4 = 20 bytes
TOS (Type of Service), 8 bits, unused
Packet length, 16 bits, (0-65535)
Identifier for fragment reassembly, 16 bits
Flags (3 bits), 1 = more fragments follow, 0 = last/only fragment
Fragmentation offset, 13 bits (0-8191)
TTL, Time To Live, 8 bits (255-0), decrement each hop, discard if 0
Upper layer protocol, 8 bits, 6 = TCP, 17 = UDP
Header checksum, 16 bits
Source IP address, 32 bits
Destination IP address, 32 bits
Options (if any), 0-10 32-bit words
Data, 0-65515 bytes

## Slide 11
Addresses
Class A: 0-127.x.x.x
Class B: 128-191.0-255.x.x
Class C: 192-223.0-255.0-255.x
Multicast: 224-239.x.x.x
Localhost: 127.0.0.1
Broadcast: x.x.x.255